## Slide 1: Attopixel imagers for physics: are these possible and useful?
Inst. of Experimental and Applied Physics
of the Czech Technical University in Prague
CERN EP Department Geneva
Erik H.M. Heijne

## Slide 2: ATTRACT proposal
SubQin4Ts
nm + ps tracking
for colliders 2030 - 2040

## Slide 3: IN ACTION on THE SQUARE MICRON
Projective ion-Beam etching
pitch lines 150 nm
overall chip was 8mmx8mm
in 1988 I was surprised
to see how big
can appear
one square micron
TU Vienna~ 1988

## Slide 4: Attopixel
very small pixels could have attofarad capacitance
10pF Si diode detector 1mm thick, 1 cm2 area
naïve linear reduction to 1 µm thick, 1µm2 area
10-12 F x 10+3 x 10-8 = 10-17 F
then ~ 1 aF for 0.3 x 0.3 µm2 area
+1 electron 1.6x 10-19 C ~160mV on 1 aF
also low electronic noise and low power

## Slide 5
for mip's
smaller capacitance allows
larger S/N
& lower power
now aim at pixel 3x3x3 µm3
voxel -
not yet attopixel !!
capacitance ~0.3fF
noise few e- rms
mip signal ~140 e-
“Conversion Gain”
fundamentals from Walter Snoeys
[also better formula for small capacitance]

## Slide 6: why small, thin (2-3µm) 3D pixel detectors ?
inherently large signal by ‘conversion gain’ Q/C
saturation for >keV energy deposit ?
low noise <<1 e- rms good S/N even for 40-80 e-
104V/cm electrical field at 2-5 V reverse bias
optimum carrier drift velocity
short collection distance little trapping?
fast ~10ps timing
low occupancy, even at >105 tracks/crossing
high cost of R&D + non-recurrent engineering
better to produce these in quantity for large area
what about radhard ? understand technology details

## Slide 7: is such a small pixel realistic ? consider progress in Si technology

## Slide 8: FinFET transistor evolution at Intel
Zheng Guo et al. Intel. ISSCC 2018 paper 11.1

## Slide 9: recent Si CMOS imagers 3 examples

## Slide 10
Wonchul Choi et al. Samsung; ISSCC 2018 paper 5.3
Samsung

## Slide 11: Samsung 0.9 µm imager with deep-etched separation
'thicker' Si : now 4µm instead 2.7µm to improve signal for red
physics does not really need pixel trenches, delta rays cross over

## Slide 12: Stacked imager Sony : ADC connected to each pixel
M. Sakakibara et al.Sony; ISSCC 2018 paper 5.1

## Slide 13
QIS Quanta Image Sensor 1.1µm
J.Ma - team of E. Fossum
Optica 4 (2017) 1474
small pixels = “jot” 1.1x1.1 µm2
sensor wafer
65nm CMOS
readout wafer
“jot cluster”
45nm CMOS
#photons
for one “jot”
two light intensities
20000 reads
each 120 µs
noise 0.17 e-

## Slide 14: physics detectors still mostly based on 1970 – 1990 technology
lithography and ion-implantation at ≥µm level
wafer size 100 – 150 mm (readout 200 mm)
signal processing in LHC used 0.25 µm CMOS upgrades now evolve to 90nm or 65nm CMOS
yet: innovative systems, produce good results

## Slide 15: 1980 Si sensor “revolutions” 1990
Si Microstrip Detectors
may cover larger area
Si Pixel Detectors
for highest particle densities
1D linear array
diodes50µm x 2-15 cm
depleted bulk ~300µm
2D pixel matrix with bumps
diodes 50µm – 500µm
depleted bulk ~150µm
30mm
500µm
pitch
75µm

## Slide 16: Pixel detectors became essential for particle physics at LHC and beyond

## Slide 17: principle of hybrid Si pixel detector/imager/solar cel? energy deposit voltage/current puls
special Si (high-ohmic)
standard Si CMOS chip

## Slide 18: ATLAS inner Si pixel layer
source: CERN- ATLAS

## Slide 19: ATLAS Si detectors nearly ready : 2008
source: CERN- ATLAS

## Slide 20: Multiple interactions in each LHC crossing
reconstruction now
possible thanks to
inner Si pixel layers
can we go to
more (even 1000?)
interactions
per crossing?
40 million ‘photos’/s
many more interactions

## Slide 21: Pixel detector development after LHC R&D continued in Medipix collaborations 1998 - now aim was to maintain/improve design expertise

## Slide 22
Timepix with brain or usual pixels without
Timepix3 (2013)
Timepix
(2006)

## Slide 23
Timepix with brain or usual pixels without
Timepix3 (2013)
Timepix
(2006)
4x1.5
6 µm
V.C. Venezia et al.
IEDM 2018
paper 10.1
BSI imager
13ke- full well
8Mpixel, dual gain
USA, OmniVision
same scale

## Slide 24: density in pixel ASICs CERN Medipix team
Chart: CMOS process [nm]
| 600.0 | 250.0 | 250.0 | 130.0 | 130.0 | 65.0 | 130.0 | 130.0
 | 0.013841 | 0.17521 | 0.18182 | 0.56198 | 0.89256 | 1.7578 | 0.6281 | 0.45455
Medipix3RX (2011)
Medipix1 (1998)
Timepix (2006)
Timepix3(2013
ClicPix (2013)
ClicPix2(2016)
VeloPix(2016
Dosepix(2010
Medipix2(2004)
Medipix4 Timepix4
slide courtesy Xavi Llopart
scale: # transistors per µm2
mm2=106 µm2
INTEL 32nm 2007

## Slide 25: hybridization is now ‘hot’ innovation for commercial CMOS imagers amazing: hybrid pixel detectors for physics are becoming disregarded and 1-tier ‘monolithic’ favored we should exploit new industrial capabilities: replace solder bumps by copper connects put more functions in multilayer chips 2-tiers, later on even 3-4 tiers

## Slide 26
Walter Snoeys on monolthic pixel detectors, March 2019

## Slide 27: hybridization is now ‘hot’ innovation for commercial CMOS imagers amazing: hybrid pixel detectors for physics are becoming disregarded and 1-tier ‘monolithic’ favored we should exploit new industrial capabilities: replace solder bumps by copper connects put more functions in multilayer chips 2-tiers, later on even 3-4 tiers

## Slide 28: Flash Memory
Hiroshi Maejima et al.Toshiba. ISSCC 2018 paper 20.1 512 Gb 3b/cell

## Slide 29: Toshiba holes
Hiroshi Maejima et al.Toshiba. ISSCC 2018 paper 20.1
Multi-layer USB memory

## Slide 30: signals of m.i.p. in thin pixel detectors particle energy loss/deposition [a brief overview]

## Slide 31: Energy loss muons in silicon
CERN Yellow Report 83-06
Bethe-Bloch
+ density effect
‘loss’ restricted < 0.5MeV
integrated Landau measured
peak Landau for ~1mm Si
and ~0.5 mm

## Slide 32: ENERGY LOSS vs ENERGY DEPOSIT
dE/dx CALCULATION SUPPOSES 'INFINITE' ABSORBER
- ALL POSSIBLE TRANSFERS HAVE TO BE REALIZED
- ALL ENERGY LOSS TO BE CONTAINED IN ABSORBER
resticted energy ‘loss’
introduce limit on energy transfer h
FOR 'THIN' ABSORBERS CORRECTION NEEDED
d ELECTRON ESCAPES
d ELECTRON CONTAINED

## Slide 33: measurements with m.i.p.s in Si (1979)
280 GeV muons
EHN2
PIONS
EHN1 beam H2
AFTER SUBTRACTION
783
522
OFTEN 2 or 3 PARTICLES
passing through diode !!!
each also follows a Landau distribution

## Slide 34: Small pitch pixels: Timepix by LHCb

## Slide 35: TYPICAL TRAILS ...
T3-1500
T3-1504
T3-1507

## Slide 36: now look at real thin pixel detectors simulations 1 - 3 - 5.6 µm measurements 5.6 – 120 µm using 12 GeV protons at grazing angle Perugia team (Passeri, Meroli, Servoli,..)

## Slide 37: Landau distribution 3 µm Si Geant4
most probable value 130 e-
width FWHM 180 e-
500
1000
0
eV
e-h pairs
eV
e-h pairs
no visible change
with readout chip
behind the thin sensor
quick simulation Lukas Tlustos

## Slide 38: Landau distribution 3 µm Si Geant4
most probable value 130 e-
width FWHM 180 e-
2nd peak is artefact
500
1000
0
eV
e-h pairs
eV
e-h pairs
no visible change
with readout chip
behind the thin sensor
+ newer simulation Lukas Tlustos

## Slide 39: Landau 3 and 1 µm Si Geant4
most probable value 130 e-
width FWHM 180 e-
500
1000
0
eV
e-h pairs
quick simulation
eV
e-h pairs
1 µm layer appears to record
some events with zero loss
really correct???
2.2% mentioned by Wang et al.
NIM A899(2018) 1-5 (ATLAS/LBL)

## Slide 40: Landau 3 and 1 µm Si Geant3
most probable value 130 e-
width FWHM 180 e-
500
1000
0
eV
e-h pairs
1 µm sensor
most probable value <40 e-
width FWHM 50 e-
eV
e-h pairs
500
1000
0
simulation Lukas Tlustos

## Slide 41
12 GeV protons in 5.6µm Si imager
Perugia group (– CMS)
Meroli et al. JINST 6 (2011) P06013
this team is also collaborating in ATTRACT proposal SubQin4Ts
black points/curve measured
well represented after convolution

## Slide 42: Landau 5.6, 3 and 1 µm Si + experiment
most probable value 130 e-
width FWHM 180 e-
500
1000
0
eV
e-h pairs
5.6 µm sensor
most probable value 270±10 e-
width FWHM 285±3 e-
Meroli et al. JINST 6 (2011) P06013
eV
e-h pairs
500
1000
0
data 12 GeV protons
Landau curves simulated
Perugia team

## Slide 43
Perugia group
Meroli et al. JINST 6 (2011) P06013
e-h pairs per µm
60
40
70
50
80
12 GeV protons in 5.6 – 120 µm Si
measured using grazing incidence along pixels

## Slide 44
Perugia group
Meroli et al. JINST 6 (2011) P06013
e-h pairs per µm
60
40
70
50
80
12 GeV protons in 5.6 – 120 µm Si
using grazing incidence along pixels
1 µm sim
simulations 1 – 3 µm added

## Slide 45: comparison with earlier data
deposit / µm is decreasing tracking mip is ONLY aim
HEIJNE
GRUHN e
CALC
--- LIMIT:mean value in thick Si 360 eV/µm ------
e-h PAIRS PER µm
+ 220 eV 25µm
eV/µm
90 --
60 --
100 --
80 --
70 --
< 1mm BINDING of ELECTRONS causes
deviation from Landau distribution: shift+widening
values for VERY thin devices: <55 e-h pairs/µm
transfers via plasmons of 20eV
bandgap 1.12eV - 3.64eV/pair
old work:
Heijne CERN 83-06 (1983) 30
+refs in there
Bak et al.
Nucl. Phys. B288 (1987) 681
more recent:
Meroli et al.
J. Instr 6 (2011) P06013
is there probability for
ZERO signal ??
Heijne CERN 83-06 (1983) 30
Meroli et al.
J. Instr 6 (2011) P06013
+ 220 eV 25µm

## Slide 46: can mip’s give zero signal in 1 µm Si layer ? as simulated by Geant4 & Allpix these use ‘Bichsel’model with ‘large’ transfers however, look at EELS results we may have to update Allpix task for SubQin4Ts

## Slide 47: The basic, small energy transfers - plasmons
MAGNETIC SPECTROMETER
Measurements of probability of only single transfer in thin Si layer
EELS Electron Energy Loss Spectroscopy
100 nm Si sheet Stiebling & Raether, Phys Rev Lett 40 (1978) 1293
25 & 480 nm Si sheets Egerton, Rep Prog Phys 72 (2009) 016502 (next slide)
  multiples of 16.7 eV plasmon energy
mean-free-path between events 115nm
no deposit in 1µm Si seems unlikely ??
E
E - e
e
o
TYPICAL TRANSFER is PLASMON with 16.7 eV
COLLECTIVE ELECTRON OSCILLATION
energy needed for bandgap ionization >1.12 eV mean e-h PAIR 3.64 eV
smaller transfers <1.12 eV can only give ’heat'
17.4 eV plasmons result inionizations + heat

## Slide 48
mean scattering length
25 nm thin Si
480 nm thin Si
first peak 16.7 eV; zero peak much reduced

## Slide 49: ATTRACT proposal
Oichi Kumagai et al., Sony
ISSCC 2018 paper 5.4
1.5 µm pixels
event driven
10b ADC
aims: checking signal generation in 1-6 µm thin Si pixels
review existing or upcoming technologies for 2(-3-4) layer stacking
find possibilities for access to such technologies

## Slide 50: Future particle imagers at colliders
advantages for 3µm pixels, also in multiple layers
<< ns signal collection improves timing precision
short signal path improves radiation hardness
reduced carrier trapping probability
high field possible even at 1-5 volts
reduction of coordinate corruptions by delta electrons
track vector parameters locally available
possibility to determine primary vertex at 1st level
....

## Slide 51: Some Conclusions
Technical innovation essential for physics progress
silicon still offers possibilities for new approaches
Electronics determines sensors and systems
'ultra'pixels implemented in advanced nanotechnologies?
Low noise achieved by sensor segmentation
segmentation is also solution for dark current, even mA
pixel detectors for high multiplicity and nm positions
Timing at ps precision is next frontier
avalanche layer or attopixels ? light is faster than electrons
Other technologies?
stacking of active layers integrated cooling
more points for more realistic imaging

## Slide 52: Future experiments will rely on newest electronics need timely R&D efforts, expertise and resources worldwide collaboration & tens of millions to do it right Thank You

## Slide 53: There's plenty of room at the bottom Richard P. Feynman 1959, APS at Caltech

## Slide 54: capacitance determination nm dimensions
Walter Snoeys
R2 distance to rear contact
large compared to thickness R1

## Slide 55: CARRIER TRANSPORT in Si and GaAs
Saturation vs temp
Carrier drift velocity vs field
carrier mobility is a function of doping, temp, field..
semiconductor detectors are INHERENTLY fast : 5 - 20 ns
speed of light still much higher 3x105 km/s 360 000 km/h
100km/s
<--- lower temp
RT

## Slide 56: End